## Slide 1: Motional Control of Loudspeakers
Sujit Malde, ela17sm, Electrical and Electronic Engineering 3rd Year Project
Second Marker Viva

## Slide 2: The Problem with Loudspeakers
Not normally controlled
Distortions and non-linearities are rife
Expensive
  Manufacturers must spend lots to make loudspeakers ‘perfect’
  Most consumers can’t buy good audio
https://audiovector.com/sr-3-avantgarde-arrete.html
£12000 excluding rest of the system!

## Slide 3: The Problem with Loudspeakers
Background theory shows that:
  Subwoofers have the most non-linearities of all the loudspeakers
  Subwoofers can have their bass response extended ’for free’
Manufacturers already spending lots on R&D to make uncompensated systems sound good
Shown: typical poor subwoofer response, -15dB down at 20Hz
Frequency / Hz
100
101
102
103

## Slide 4: The solution
Open- and closed-loop compensators
Electronic solution is cheap, easy to manufacture and install
Fewer distortions, fewer non-linearities = cleaner sound reproductions
‘Free’ extension of bass response = better sound from the same physical system

## Slide 5: The process
Ideally:
Choose a subwoofer
Make an enclosure for the subwoofer
Open-loop compensator:
  Design
  Build
Closed-loop compensator:
  Design
  Build
Testing and tuning throughout

## Slide 6: Choosing a subwoofer
https://www.thompsonsltd.co.uk/touring-and-leisure/plpw6d-pyle-plpw6d-6.5-600-watt-dual-voice-coil-4-ohm-subwoofer.html

## Slide 7: Enclosure design
Background theory shows that loudspeakers can be modelled as equivalent electrical circuits:
Red indicates voice coil circuit parameters
Blue indicates equivalent circuit parameters for the driver mechanical circuit
Green indicates equivalent circuit parameters for the box mechanical circuit
Electrical and mechanical circuits can be thought of as primary and secondary of a transformer with turns ratio equivalent to Bl factor of driver magnet
Useful for SPICE/MATLAB but not easy information for end-users to digest – Thiele/Small parameters used instead

## Slide 8: Enclosure Design
Take T/S parameters from manufacturer
Convert to electromechanical equivalent circuit
Add in box circuit elements
Refine

## Slide 9: Impedance Measurements
All different permutation of connections were made and measured:
  Series
  Parallel (in 1 out 2)
  Anti-parallel (in 2 out 1)
Replace manufacturer given T/S parameters with these – also yields more accurate Bl

## Slide 11: Open-loop circuit design – Linkwitz Transform
For a loudspeaker in an enclosure:
  Brings up magnitude response
  Reduces group delay
Easy to design, made trivial using resources on the late designer’s website
Gain / dB
Frequency / Hz
f2
f1
f0
Q0

## Slide 12: Results
Group delay of the system improved for most of the range of operation
Improvement by as much as 2ms around 45Hz
System will respond faster to an input, reach a nominal value faster
As expected, magnitude response improved massively at low frequencies
In practice this is unobtainable because too much air needs to be moved, cone displacement will exceed maximum allowed value

## Slide 13: Results
Simulink model confirms that existing setup of Linkwitz Transform, driver, box does not exceed physical limitations
Important result – LT may not have worked for this driver

## Slide 14: Plans
Finish building subwoofer system
Make and test open-loop compensator
Design, simulate, build closed-loop compensators

## Slide 15: Developing Technologies
FPAA (e.g. as made by Anadigm) - easy interfacing with MATLAB/Simulink, mini DSP
Different loudspeaker types other than simple coil-and-cone:
  Electrostatic topology
  Planar magnetic topology
Each has their own advantages and disadvantages
Most useful innovations are patented!

## Slide 16
Thank you for listening, any questions?